## Slide 1: Back-off Algorithm for CSMA/CD

## Slide 2: Back-off Algorithm for CSMA/CD
Back-off algorithm is a collision resolution mechanism which is used in CSMA/CD.
This algorithm is generally used in Ethernet to schedule re-transmissions after collisions.

## Slide 3: Problem
If a collision takes place between 2 stations, they may restart transmission as soon as they can after the collision.
This will always lead to another collision and form an infinite loop of collisions leading to a deadlock.
To prevent such scenario back-off algorithm is used.

## Slide 4
Let us consider an scenario of 2 stations A and B transmitting some data:

## Slide 5
After a collision, time is divided into discrete slots (Tslot) whose length is equal to 2t, where t is the maximum propagation delay in the network.
The stations involved in the collision randomly pick an integer from the set K i.e {0, 1}. This set is called the contention window.
If the sources collide again because they picked the same integer, the contention window size is doubled and it becomes {0, 1, 2, 3}.
Now the sources involved in the second collision randomly pick an integer from the set {0, 1, 2, 3} and wait that number of time slots before trying again. Before they try to transmit, they listen to the channel and transmit only if the channel is idle. This causes the source which picked the smallest integer in the contention window to succeed in transmitting its frame.

## Slide 6: Algorithm
So, Back-off algorithm defines a waiting time for the stations involved in collision, i.e. for how much time the station should wait to re-transmit.
Waiting time = back–off time
Let n = collision number.
Then,
Waiting time = K * Tslot
where K = [0, 2n – 1 ]

## Slide 7: How it works?
Case-1 :
Suppose 2 stations A and B start transmitting data (Packet 1) at the same time then, collision occurs. So, the collision number n for both their data (Packet 1) = 1. Now, both the station randomly pick an integer from the set K i.e. {0, 1}.

## Slide 8
When both A and B choose K = 0
  Waiting time for A = 0 * Tslot = 0 Waiting time for B = 0 * Tslot = 0 Therefore, both stations will transmit at the same time and hence collision occurs.
When A chooses K = 0 and B chooses K = 1
  Waiting time for A = 0 * Tslot = 0 Waiting time for B = 1 * Tslot = Tslot Therefore, A transmits the packet and B waits for time Tslot for transmitting and hence A wins.
When A chooses K = 1 and B chooses K = 0 Waiting time for A = 1 * Tslot = Tslot Waiting time for B = 0 * Tslot = 0 Therefore, B transmits the packet and A waits for time Tslot for transmitting and hence B wins.
When both A and B choose K = 1 Waiting time for A = 1 * Tslot = Tslot Waiting time for B = 1 * Tslot = Tslot Therefore, both will wait for the same time Tslot and then transmit. Hence, collision occurs.

## Slide 9
Probability that A wins = 1/4
Probability that B wins = 1/4
Probability of collision = 2/4

## Slide 10
Case-2 :
Assume that A wins in Case 1 and transmitted its data (Packet 1). Now, as soon as B transmits its packet 1, A transmits its packet 2. Hence, collision occurs. Now collision no. n becomes 1 for packet 2 of A and becomes 2 for packet 1 of B.
For packet 2 of A, K = {0, 1} For packet 1 of B, K = {0, 1, 2, 3}
Probability that A wins = 5/8
Probability that B wins = 1/8
Probability of collision = 2/8

## Slide 11
So, probability of collision decreases as compared to Case 1.
Advantage –
  Collision probability decreases exponentially.
Disadvantages –
  Capture effect: Station who wins ones keeps on winning.
  Works only for 2 stations or hosts.

## Slide 12
A and B are the only two stations on an Ethernet. Each has a steady queue of frames to send. Both A and B attempt to transmit a frame, collide, and A wins the first backoff race. At the end of this successful transmission by A, both A and B attempt to transmit and collide. The probability that A wins the second backoff race is: