## Slide 1
Chapter 1
Introduction

## Slide 2
DATA COMMUNICATIONS
The term telecommunication means communication at a distance. The word data refers to information presented in whatever form is agreed upon by the parties creating and using the data. Data communications are the exchange of data between two devices via some form of transmission medium such as a wire cable.
Topics discussed in this section:
Components of a data communications system
Data Flow

## Slide 3: DATA COMMUNICATIONS
The effectiveness of data communication depends on four fundamental characteristics:
-- delivery
-- accuracy
-- timeliness
-- jitter

## Slide 4
Figure 1.1 Components of a data communication system

## Slide 5
DATA REPRESENTATIONS
Text
Numbers
Images
Audio
Video

## Slide 6
Figure 1.2 Data flow (simplex, half-duplex, and full-duplex)

## Slide 7
NETWORKS
A network is a set of devices (often referred to as nodes) connected by communication links. A node can be a computer, printer, or any other device capable of sending and/or receiving data generated by other nodes on the network. A link can be a cable, air, optical fiber, or any medium which can transport a signal carrying information.
Network Criteria
Physical Structures
Categories of Networks
Topics discussed in this section:

## Slide 8
Network Criteria
Performance
  Measured in terms of Delay and Throughput
  Measured in accordance with transit and response time
  Performance of network is dependent on
    Number of users,
    Types of transmission medium used,
    Capabilities of connected hardware,
    Efficiency of software.
Reliability
  Failure rate of network components
  Measured in terms of availability/robustness
Security
  Data protection against corruption/loss of data due to:
      Errors
      Malicious users

## Slide 9
Physical Structures
Type of Connection
  Point to Point - single transmitter and receiver
  Multipoint - multiple recipients of single transmission
Physical Topology
  Connection of devices
  Type of transmission - unicast, mulitcast, broadcast

## Slide 10
Figure 1.3 Types of connections: point-to-point and multipoint

## Slide 11
Network Topology
The term network topology refers to the way in which a network is laid out physically.
The topology of a network is the geometrical representation of the relationship of all the links and linking devices (usually called nodes) to one another.
There are 4 basic topologies possible --

## Slide 12
Figure 1.4 Categories of topology

## Slide 13
Figure 1.5 A fully connected mesh topology (five devices)

## Slide 14
In this topology, every device has a dedicated point-to-point link to every other device.
The term dedicated means that the link carries traffic only between the two devices it connects.
To find the number of physical links in a fully connected mesh network with ‘n’ nodes, Node 1 must be connected to every other (n-1) nodes, likewise Node 2 must be connected to every other (n-1) nodes … and finally Node N must be connected to every other (n-1) nodes. Hence, total number of physical links will be n(n-1).
If each physical link allows communication in both directions (duplex mode), we can divide the number of links by 2, i.e., in mesh topology, we need n(n-1)/2 duplex mode links.
To accommodate these many links, every device on network must have n-1 I/O ports to be connected to the other n-1 stations.

## Slide 15
Advantages of Mesh Topology
-- the use of dedicated links guarantees that each connection can carry its own data load, thus eliminates traffic problems.
-- mesh links are robust, because, if one link becomes unusable (broken), it does not incapacitate the entire system.
-- privacy/security, because, when every message travels along a dedicated link, only the intended recipients receives it.
Disadvantages of Mesh Topology
-- amount of cabling and number of I/O ports required is very high.
-- installation and reconnections are difficult.
-- hardware requirements are very high.
* One practical example of a mesh topology is the connection of telephone regional offices in which each regional office needs to be connected to every other regional office

## Slide 16
Assume six devices are arranged in a mesh topology. How many cables are needed? How many ports are needed for each device?

## Slide 17
Figure 1.6 A star topology connecting four stations

## Slide 18
Each device has a dedicated point-to-point link only to a central controller, usually called a hub.
The devices are not directly linked to one another. Unlike a mesh topology, a star topology does not allow direct traffic between devices.
The controller acts as an exchange: If one device wants to send data to another, it sends the data to the controller, which then relays the data to the other connected device.
Advantages of Star topology
A star topology is less expensive than a mesh topology. In a star, each device needs only one link and one I/O port to connect it to any number of others.
This factor also makes it easy to install and reconfigure. Far less cabling needs to be housed.
Other advantages include robustness. If one link fails, only that link is affected. All other links remain active. This factor leads to easy fault identification and fault isolation.

## Slide 19
Disadvantages of Star topology
One big disadvantage of a star topology is the dependency of the whole topology on one single point, the hub. If the hub goes down, the whole system is dead.
* The star topology is used in local-area networks (LANs). High-speed LANs often use a star topology with a central hub.

## Slide 20
Figure 1.7 A bus topology connecting three stations

## Slide 21
A bus topology is based on multipoint connections. One long cable acts as a backbone to link all the devices in a network.
Nodes are connected to the bus cable by drop lines and taps.
A drop line is a connection between the device and the main cable.
A tap is a connector that either splices into the main cable or punctures the sheathing of a cable to create a contact with the metallic core.
As a signal travels along the backbone, some of its energy is transformed into heat. Therefore, it becomes weaker and weaker as it travels farther and farther.
For this reason there is a limit on the number of taps a bus can support and on the distance between those taps.

## Slide 22
Advantages of Bus Topology
Ease of installation.
A bus uses less cabling than mesh or star topologies.
Disadvantages of Bus Topology
difficult reconnection and fault isolation.
difficulty in adding new devices in the system.
signal reflection at the taps can cause degradation in quality.
this degradation can be controlled by limiting the number and spacing of devices connected to a given length of cable.
adding new devices may therefore require modification or replacement of the backbone.
a fault or break in the bus cable stops all transmission, even between devices on the same side of the problem. The damaged area reflects signals back in the direction of origin, creating noise in both directions.

## Slide 23
Figure 1.8 A ring topology connecting six stations

## Slide 24
In a ring topology, each device has a dedicated point-to-point connection with only the two devices on either side of it.
A signal is passed along the ring in one direction, from device to device, until it reaches its destination.
Each device in the ring incorporates a repeater. When a device receives a signal intended for another device, its repeater regenerates the bits and passes them along.

## Slide 25
Figure 1.9 A hybrid topology: a star backbone with three bus networks

## Slide 26: What should you consider when choosing a network topology?
Available H/W
Size of N/W
Budget Limitations
Need for Reliability
Network expansion is likely to be required

## Slide 27
Categories of Networks
Local Area Networks (LANs)
  Short distances
  Designed to provide local interconnectivity
Wide Area Networks (WANs)
  Long distances
  Provide connectivity over large areas
Metropolitan Area Networks (MANs)
  Provide connectivity over areas such as a city, a campus

## Slide 28
1-4 PROTOCOLS
A protocol is synonymous with rule. It consists of a set of rules that govern data communications. It determines what is communicated, how it is communicated and when it is communicated. The key elements of a protocol are syntax, semantics and timing
Syntax
Semantics
Timing
Topics discussed in this section:

## Slide 29
Elements of a Protocol
Syntax
  Structure or format of the data
  Indicates how to read the bits - field delineation
Semantics
  Interprets the meaning of the bits
  Knows which fields define what action
Timing
  When data should be sent and what
  Speed at which data should be sent or speed at which it is being received.

## Slide 30
Name the four basic network topologies, and cite an advantage of each type.
What is the difference between half-duplex and full-duplex transmission modes?
For n devices in a network, what is the number of cable links required for a mesh, bus, and star topology?

## Slide 31
For each of the following four networks, discuss the consequences if a connection fails.
  Five devices arranged in a mesh topology.
    If one connection fails, the other connections will still be working
  Five devices arranged in a star topology (not counting the hub).
    The other devices will still be able to send data through the hub; there will be no access to the device which has the failed connection to the hub.
  Five devices arranged in a bus topology.
    All transmission stops if the failure is in the bus. If the drop-line fails, only the corresponding device cannot operate.